## Slide 1: FIGARO: Improving System Performance via Fine-Grained In-DRAM Data Relocation and Caching
Yaohua Wang1, Lois Orosa2, Xiangjun Peng3,1, Yang Guo1,
Saugata Ghose4,5, Minesh Patel2, Jeremie S. Kim2, Juan Gómez Luna2, Mohammad Sadrosadati6, Nika Mansouri Ghiasi2, Onur Mutlu2,5
MICRO 2020
1
2
3
4
5
6
Notes: Thank you very much

## Slide 2: Motivation and Goal
Problem: DRAM latency is a performance bottleneck for many applications
In-DRAM caches mitigate this latency
  by augmenting regular-latency DRAM with small-but-fast regions of DRAM that serve as a cache
Existing in-DRAM caches have mechanisms for relocating data that have two main inefficiencies:
  Coarse-grained (i.e., multi-kilobyte) in-DRAM data relocation
  Relocation latency increases with the physical distance between the slow and fast regions
Goal: reduce DRAM latency via an in-DRAM cache that provides
  Fine-grained (i.e., multi-byte) data relocation
  Distance-independent relocation latency

## Slide 3: FIGARO Substrate
FIGARO leverages existing shared structures within a modern DRAM device to perform data relocation
Observations:
  All local row buffers (LRBs) in a bank are connected to a single shared global row buffer (GRB)
  The GRB has smaller width (e.g., 8B) than the LRBs (e.g., 1kB)
Key Idea: use the existing shared GRB among subarrays within a DRAM bank to perform fine-grained in-DRAM data relocation
DST: Subarray B
B0
B1
B2
B3
B4
B5
B6
B7
SRC: Subarray A
A4
A5
A6
A7
A0
A1
A2
A3
Local Row Buffer
(LRB)
Local Row Buffer
(LRB)
GRB
A3
1kB
8B
3

## Slide 4: FIGCache (Fine-Grained In-DRAM Cache)
Key idea: cache only small, frequently-accessed portions of different DRAM rows in a designated region of DRAM
FIGCache uses FIGARO to relocate data into and out of the cache at fine granularity
Results:
  Improves system performance by 16.3% on average
  Reduces DRAM energy by 7.8% on average
  Outperforms a state-of-the-art coarse-grained in-DRAM cache
  Performs close to ideal low-latency DRAM
4

## Slide 5: FIGARO: Improving System Performance via Fine-Grained In-DRAM Data Relocation and Caching
Yaohua Wang1, Lois Orosa2, Xiangjun Peng3,1, Yang Guo1,
Saugata Ghose4,5, Minesh Patel2, Jeremie S. Kim2, Juan Gómez Luna2, Mohammad Sadrosadati6, Nika Mansouri Ghiasi2, Onur Mutlu2,5
MICRO 2020
1
2
3
4
5
6
Notes: Thank you very much