## Slide 1: Reducing Solid-State Drive Read Latency by Optimizing Read-Retry
Jisung Park1, Myungsuk Kim2, Myoungjun Chun2, Lois Orosa1, Jihong Kim2, and Onur Mutlu1
ASPLOS 2021 (Session 17: Solid State Drives)
1
2

## Slide 2: Executive Summary
Problem: Long read latency in modern SSDs due to read-retry
  Multiple retry steps required to read an erroneous page
  Read-retry frequently occurs in modern NAND flash memory
Goal: Reduce the latency of each read-retry operation
Key Ideas:
  Pipelined Read-Retry (PR2): Concurrently perform consecutive retry steps using the CACHE READ command
  Adaptive Read-Retry (AR2): Reduce read-timing parameters for every retry step by exploiting the reliability margin provided by strong ECC
Evaluation Results: Our proposal improves SSD response time by
  Up to 51% (35% on average) compared to a high-end SSD
  Up to 32% (17% on average) compared to a state-of-the-art baseline

## Slide 3: Talk Outline
Read-Retry in Modern NAND Flash-Based SSDs
PR2: Pipelined Read-Retry
AR2: Adaptive Read-Retry
Evaluation Results
Read-Retry in Modern NAND Flash-Based SSDs
PR2: Pipelined Read-Retry
AR2: Adaptive Read-Retry
Evaluation Results

## Slide 4: Errors in NAND Flash Memory
…
Number of Cells
Px state
P(x-1) state
…
P(x+1) state
V
REF(x-1)
V
REFx
V
TH
Cell’s Threshold Voltage ( )
V
REF(x-2)
V
REF(x+1)
Read-Reference Voltage
NAND flash memory stores data by using cells’ VTH values

## Slide 5: Errors in NAND Flash Memory
…
Number of Cells
Px state
P(x-1) state
…
P(x+1) state
V
REF(x-1)
V
REFx
V
TH
Cell’s Threshold Voltage ( )
V
REF(x-2)
V
REF(x+1)
Various sources shift and widen programmed VTH states
  Retention loss, program interference, read disturbance, etc.
Retention loss
Interference/disturbance
# of error cells > ECC correction capability  Uncorrectable errors in stored data
Error cells

## Slide 6: Read-Retry Operation
Reads the page again with adjusted VREF values
…
Number of Cells
Px state
P(x-1) state
…
P(x+1) state
V
REF(x-1)
V
REFx
V
TH
Cell’s Threshold Voltage ( )
V
REF(x-2)
V
REF(x+1)

## Slide 7: Read-Retry Operation
Reads the page again with adjusted VREF values
…
Number of Cells
Px state
P(x-1) state
…
P(x+1) state
V
REF(x-1)
V
REFx
V
TH
Cell’s Threshold Voltage ( )
V
REF(x-2)
V
REF(x+1)
V’
REF(x-2)
V’
REF(x-1)
V’
REFx
V’
REF(x+1)
Error cells
Read using properly-adjusted VREF values
 Decreases # of raw bit errors
Read-retry: Adjusting VREF values

## Slide 8: Read-Retry: Performance Overhead
NERR = 32
< ECC capability CECC = 72
READ A
tREAD
tR: Page sensing
tDMA: Data transfer
tECC: ECC decoding

## Slide 9: Read-Retry: Performance Overhead
tR
tDMA
tECC
ECC Capability CECC= 72
Read-retry increases the read latency
almost linearly with the number of retry steps
READ A
NERR= 232
tREAD
RR1
NERR= 173
RR(N – 1)
RRN
⋯
⋯
tRETRY
NERR= 87
NERR= 23
= N×(tR+tDMA+tECC)
NERR= 118
RR2

## Slide 10: Talk Outline
Read-Retry in Modern NAND Flash-Based SSDs
PR2: Pipelined Read-Retry
AR2: Adaptive Read-Retry
Evaluation Results

## Slide 11: PR2: Pipelined Read-Retry
tR
tECC
tDMA
ECC Capability CECC= 72
RR1
RR(N – 1)
RRN
⋯
⋯
tRETRY
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 23
= N×(tR+tDMA+tECC)
NERR= 118
RR2
Key idea: Concurrently perform consecutive retry steps

## Slide 12: PR2: Pipelined Read-Retry
tR
tECC
tDMA
ECC Capability CECC= 72
RR1
RR(N – 1)
RRN
⋯
⋯
tRETRY
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 23
= N×(tR+tDMA+tECC)
NERR= 118
RR2
Key idea: Concurrently perform consecutive retry steps
CACHE READ

## Slide 13: PR2: Pipelined Read-Retry
tR
tECC
tDMA
ECC Capability CECC= 72
RR1
RR(N – 1)
RRN
⋯
⋯
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 23
NERR= 118
RR2
Key idea: Concurrently perform consecutive retry steps
CACHE READ
tRETRY’
= N×tR+tDMA+tECC
Latency reduction
PR2: Removes tDMA & tECC (~30% of each retry step) from the critical path

## Slide 14: Talk Outline
Read-Retry in Modern NAND Flash-Based SSDs
PR2: Pipelined Read-Retry
AR2: Adaptive Read-Retry
Evaluation Results

## Slide 15: AR2: Adaptive Read-Retry
tR
tECC
tDMA
ECC Capability CECC= 72
RR1
RR(N – 1)
RRN
⋯
⋯
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 118
RR2
tRETRY’
= N×tR+tDMA+tECC
NERR= 23

## Slide 16: AR2: Adaptive Read-Retry
tR
tECC
tDMA
RR1
RR(N – 1)
RRN
⋯
⋯
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 118
RR2
tRETRY’
= N×tR+tDMA+tECC
NERR= 23
ECC Capability CECC= 72
Observation: A positive ECC margin in the final retry step when read-retry succeeds

## Slide 17: AR2: Adaptive Read-Retry
tR
tECC
tDMA
RR1
RR(N – 1)
RRN
⋯
⋯
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 118
RR2
Key idea: Reduce read-timing parameters for every retry step
tRETRY’
= N×tR+tDMA+tECC
NERR= 23
ECC Capability CECC= 72
ρ× tR (0<ρ<1)

## Slide 18: AR2: Adaptive Read-Retry
tR
tECC
tDMA
RR1
RR(N – 1)
RRN
⋯
⋯
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 118
RR2
Key idea: Reduce read-timing parameters for every retry step
NERR= 23
ECC Capability CECC= 72
ρ× tR (0<ρ<1)
tRETRY’
= N×ρ×tR+tDMA+tECC
Latency reduction

## Slide 19: AR2: Adaptive Read-Retry
tR
tECC
tDMA
RR1
RR(N – 1)
RRN
⋯
⋯
READ A
NERR= 232
tREAD
NERR= 173
NERR= 87
NERR= 118
RR2
Key idea: Reduce read-timing parameters for every retry step
NERR= 23
ECC Capability CECC= 72
ρ× tR (0<ρ<1)
tRETRY’
= N×ρ×tR+tDMA+tECC
+α
+α
+α
+α
+α
(additional errors)
Latency reduction
Needs to ensure that # of additional errors < ECC margin

## Slide 20: Validation with Real 3D NAND Flash Chips
160 real 48-layer Triple-Level Cell (TLC) NAND flash chips
Observation 1: A large ECC margin in the final retry step even under worst-case operating conditions
  Max. 40 errors per KiB under 1-year retention @ 2K P/E cycles
Observation 2: A large reliability margin incorporated in read-timing parameters
  25% tR reduction  Max. 23 additional errors
AR2 can easily work in state-of-the-art NAND flash chips w/ at least 25% tR reduction

## Slide 21: Talk Outline
Read-Retry in Modern NAND Flash-Based SSDs
PR2: Pipelined Read-Retry
AR2: Adaptive Read-Retry
Evaluation Results

## Slide 22: Evaluation Results
  Simulation using MQSim [Tavakkol, FAST18] and 12 real workloads
  Our proposal improves SSD response time by
    Up to 51% (35% on average) compared to a high-end SSD w/o read-retry mitigation
    Up to 32% (17% on average) compared to a state-of-the-art read-retry mitigation technique
  Many more detailed studies in the paper

## Slide 23: Reducing Solid-State Drive Read Latency by Optimizing Read-Retry
Jisung Park1, Myungsuk Kim2, Myoungjun Chun2, Lois Orosa1, Jihong Kim2, and Onur Mutlu1
ASPLOS 2021 (Session 17: Solid State Drives)
1
2