## Slide 1: Understanding RowHammer Under Reduced Wordline Voltage An Experimental Study Using Real DRAM Devices Session 14 (June 30, 10:30 AM) Hardware and Software Security
Abdullah Giray Yağlıkçı
Haocong Luo Geraldo F. de Oliviera Ataberk Olgun
Minesh Patel Jisung Park Hasan Hassan Jeremie S. Kim
Lois Orosa Onur Mutlu
Notes: Hello, I am Giray, and this is the lightning talk for our new paper Understanding RowHammer Under Reduced Wordline Voltage

## Slide 2: Executive Summary
Motivation:
  Repeatedly toggling a DRAM row’s wordline voltage causes bit flips in nearby rows
  This vulnerability, RowHammer, worsens in denser DRAM chips
  Understanding RowHammer enables designing effective and efficient solutions
Problem: No study demonstrates how wordline voltage (VPP) affects RowHammer
Goal: Experimentally understand how VPP affects RowHammer and DRAM operation
Experimental study: 272 DRAM chips from three major manufacturers
VPP’s effect on RowHammer: Six observations show that with reduced VPP,
    A row needs to be hammered 7.4% more times (85.8% max) to induce a bit flip
    Bit error rate caused by a RowHammer attack reduces by 15.2% (66.9% max)
VPP’s effect on DRAM operation: Nine observations show that with reduced VPP,
  208 out of 272 tested DRAM chips reliably operate using nominal timing parameters
  Erroneous DRAM chips can reliably operate with
      A longer row activation latency, i.e., 24ns/15ns for 48/16 chips,
      Single-error-correcting codes or 2x the refresh rate only for 16.4% of rows
Conclusion: Scaling down the wordline voltage can reduce RowHammer vulnerability without significantly affecting reliable DRAM operation
Notes: Repeatedly toggling a DRAM row’s wordline voltage causes bit flips in nearby rows, breaking the memory isolation. [CLICK]
This vulnerability, called RowHammer, worsens in denser DRAM chips [CLICK]
And Understanding RowHammer is critical to find effective and efficient solutions. [CLICK]
However, no prior study demonstrates how this vulnerability varies with wordline voltage: VPP[CLICK]
In this work, our goal is to experimentally understand how VPP affects RowHammer and reliable DRAM operation [CLICK]
To this end, we test 272 real DDR4 DRAM chips from three major manufacturers [CLICK]
Based on our analyses, we make SIX observations showing a reduction in RowHammer vulnerability by scaling down VPP such that[CLICK]
inducing a bit flip requires larger hammer counts [CLICK]
and bit error rate due to a RowHammer attack significantly reduces [CLICK]
To assess VPP's effect on reliable DRAM operation, we make NINE observations showing that [CLICK]
Most of the tested DRAM chips reliably operate at reduced VPP using nominal timing parameters [CLICK]
And the erroneous DRAM chips can still reliably operate with [CLICK]
a longer row activation latency [CLICK]
And when used with a SIMPLE single error correcting code or double the refresh rate for a small fraction of DRAM rows [CLICK]
Based on our findings, we conclude that scaling down the wordline voltage can reduce RowHammer vulnerability without significantly affecting reliable DRAM operation [END]

## Slide 3: Understanding RowHammer Under Reduced Wordline Voltage An Experimental Study Using Real DRAM Devices Session 14 (June 30, 10:30 AM) Hardware and Software Security
Abdullah Giray Yağlıkçı
Haocong Luo Geraldo F. de Oliviera Ataberk Olgun
Minesh Patel Jisung Park Hasan Hassan Jeremie S. Kim
Lois Orosa Onur Mutlu
Notes: Please attend our full talk at Session 14 on June 30th if you are interested!