## Slide 1: ITAP: Idle-Time-Aware Power Management for GPU Execution Units
Mohammad Sadrosadati | Seyed Borna Ehsani
Hajar Falahati | Rachata Ausavarungnirun
Arash Tavakkol | Mojtaba Abaee
Lois Orosa Hamid Sarbazi-Azad | Yaohua Wang Onur Mutlu

## Slide 2: Executive Summary
Motivation: GPU execution units are frequently idle
  Full-lane and partial-lane idleness
  High static power
Problem: static energy represents a high percentage of the energy consumption on execution units
Key idea: Employ the most efficient power management mode for each idle period
Mechanism: Predict the idle period length and apply power-gating and different levels of voltage-scaling
Results:
  27.6% more static energy savings than the state-of-the-art mechanisms
  Less than 2.1% performance overhead

## Slide 3: Outline
ion and Goal
Background
Motivation
Inefficiency of Prior Works
ITAP
Evaluation
Conclusion
Notes: Here is the outline for the talk today [CLICK]

## Slide 4: Outline
ion and Goal
Background
Motivation
Inefficiency of Prior Works
ITAP
Evaluation
Conclusion
Notes: Here is the outline for the talk today [CLICK]

## Slide 5: GPU Background
Groups of threads are assigned to a Streaming Multiprocessor (SM)
  Single Instruction Multiple Data (SIMD) execution units
Threads within the SMs are divided into warps
Threads inside a warp are executed in parallel lock-step manner
  All threads execute the same instruction
SIMD units are time-multiplexed between different warps
A SIMD lane executes the instructions of a thread

## Slide 6: Static Power Reduction Techniques
The contribution of the static power to total power consumption is significant (e.g. 20% on an NVIDIA GTX 480 [Leng+ ISCA’13])
Sleep mode: reduces the power supply
  The execution units do not function properly
Wake-up: the power supply is switched back to full in order to gain functionality
  Twake_up : wake-up time
  Ewake_up : wake-up energy
Tbreak_even : minimum idle time for that the energy savings can break even with the energy overhead of wake-up

## Slide 7: Sleep Modes
Two main sleep modes:
  Power-gating (PG)
    Cuts off the supply voltage entirely
    Sleep transistor between the voltage supply line and the pull up network
    Tbreak_even = 14 cycles
  Voltage-scaling (VS)
    Uses voltage regulators
    Tbreak_even = 1-2 cycles (VS0.3-VS0.5)

## Slide 8: Outline
ion and Goal
Background
Motivation
Inefficiency of Prior Works
ITAP
Evaluation
Conclusion
Notes: Here is the outline for the talk today [CLICK]

## Slide 9: GPU Execution Units Are Frequently Idle
Why?
Partial-lane idleness
  Branch divergence: when threads on a warp take different control flow paths
Full-lane idleness
  There are no active warps to be scheduled for execution (e.g., memory accesses)
Around 53%

## Slide 10: What Is The Main Challenge?
Dealing with different idle period lengths
Goal: cover 100% of idle periods
in an efficient way
PG is not effective:
  The length of the idle periods is shorter than Tbreak_even in most of the cases
Prior works do not cover all idle period sizes
95.9%

## Slide 11: Outline
ion and Goal
Background
Motivation
Inefficiency of Prior Works
ITAP
Evaluation
Conclusion
Notes: Here is the outline for the talk today [CLICK]

## Slide 12: Prior Works
We will show the inefficiency of prior works
in two cases:
  Partial-lane idleness
  Full-lane idleness

## Slide 13: Partial-Lane Idleness
35% of warps are under-utilized
NN & MUM usually have 1-4 active threads
Prior solutions
Reducing lane size [Vaidya+ ISCA’13]  performance overhead
Thread block compaction [Fung+ HPCA’11] limited opportunity
35%
Active threads in a warp

## Slide 14: Full-Lane Idleness
Criticality-Aware Warp Scheduler (CAWS) [Lee+ PACT’14]: prioritize slower warps
Progress-Aware Warp Scheduler (PRO) [Anantpur+ IPDPS’15]: prioritize warps based on their progress
Max TLP: maximum (ideal) Thread Level Parallelism
Max TLP+Throttling: Max TLP + a state-of-the-art throttling mechanism to mitigate the contention caused by higher TLP
Max TLP+2x Bandwidth: double on/off-chip bandwidth
42% full-lane idleness for the baseline GPU
35% full-lane idleness even after using state-of-the-art warp schedulers (CAWS & PRO)
Reducing leakage power of idle execution lanes is very important
Even the ideal techniques have
significant full-lane idleness

## Slide 15: Outline
ion and Goal
Background
Motivation
Inefficiency of Prior Works
ITAP
Evaluation
Conclusion
Notes: Here is the outline for the talk today [CLICK]

## Slide 16: ITAP: Idle-Time-Aware Power Management
Observation:
The best static power reduction technique depends on the length of the idle period
Key ideas:
Classify the idle periods on types (i.e., short, medium, or long periods)
Assign each type to the most effective power reduction technique
  Short idle periods  Voltage-scaling to 0.5VDD
  Medium idle periods  Voltage-scaling to 0.3VDD
  Long idle periods  Power-gating
Predict idle period types
Use a peek-ahead approach for improving performance

## Slide 17: Power Reduction Techniques
0.5v is the best for idle periods “<=4”
0.3v is the best for idle periods “5-44”
PG is the best for idle periods “>44”

## Slide 18: Predicting Idle Period Type
Finite State Machine (FSM) with four states to predict the idle period type
  One active state
  Three sleep mode states
Two counters:
  Mode-change counter (countermode):
    Keeps or changes the mode
    Thrswitch is the threshold for switching the mode
    Incremented when the idle time is > 8 cycles
  Confidence Counter (counterconf):
    Differentiates between medium and long periods
    Thrlong is the threshold for switching to a long period
    Decremented if the idle time is < 48 cycles
ON
PG
VS
0.5
VS
0.3

## Slide 19: ITAP’s FSM
ON
PG
VS
0.5
VS
0.3
T1
T2
T3
T4
T5
T6
T7
T8
T9
T10
T8: The lane is idle
T10: The lane is idle
T4: lane idle for less than 4 cycles or countermode < Thrswitch
T5:
  lane idle for more than 4 cycles
  countermode > Thrswitch
  counterconf < Thrlong
T6:
  lane idle for more than 4 cycles
  countermode > Thrswitch
  counterconf > Thrlong
T1: The lane is active
T2: The lane is idle
T3: The lane is active
T7: The lane is active
T9: The lane is active
ON remains while the lane is active
VS0.3 and PG remain
while the lane is idle
When a lane changes from active to idle,
ITAP always applies VS0.5
If the lane is idle, VS0.5 remains or changes depending on the counters
When a lane changes from idle to active,
ITAP always exits the sleep modes

## Slide 20: ITAP Issues
Our mechanism has two issues
  ITAP always selects VS0.5 mode first, no matter the length of the idle period
    Room for optimization
  ITAP can not figure out when an execution lane should be woken up ahead of time
    Performance overhead due to Twake_up
To solve these issues, we propose a peek-ahead technique

## Slide 21: Peek-Ahead Window
Goal: know the state of the lane in the near future
Implementation:
  A 3-cycle peek-ahead window
  Slightly modify the round-robin warp scheduler
  Determine two future warps to schedule in addition to the currently-selected warp
Result: hides the wake-up latency of each power reduction technique
  One cycle for 0.5v
  Two cycles for 0.3v
  Three cycles for PG
More details in the paper

## Slide 22: ITAP Granularity
ITAP can be applied to each lane individually or use the same reduction mode for all of idle lanes
Fine-grain implementation
  Apply power reduction technique for each idle lane individually
  Different lanes can be in different power reduction modes
  Higher accuracy
  Larger overhead (due to per-lane voltage regulators)
Coarse-grain implementation
  Apply one power reduction for all idle lanes
  Lower accuracy
  Lower overhead
How to select the power reduction mode for all idle lanes?

## Slide 23: ITAP Coarse-grain implementation
The ITAP algorithm to select the power mode is applied to every single lane
0.5
If any idle execution lane is selected to be in VS0.5 mode
then the selected power mode for all idle lanes is VS0.5
If no idle execution lane in VS0.5 and at least one idle execution lane in VS0.3
then the selected power mode for all idle lanes is VS0.3
If all lanes are selected to be in PG mode
then the selected power mode for all idle lanes is PG

## Slide 24: Outline
ion and Goal
Background
Motivation
Inefficiency of Prior Works
ITAP
Evaluation
Conclusion
Notes: Here is the outline for the talk today [CLICK]

## Slide 25: Evaluation Methodology
Simulator: GPGPU-Sim [Bakhoda+ ISPASS’09] modeling NVIDIA Pascal
Energy: GPUWattch [Leng+ ISCA’13] and HSPICE
19 Workloads from Rodinia, Parboil and ISPASS benchmark suites
Comparison points:
  Conventional Power-Gating (CPG)
  Pattern-aware warp scheduling (PATS) [Xu+ PACT’14]
    State-of-the-art scheduler-aware PG technique
  Variants of ITAP
    Ideal
    With and without peek-ahead
    Power aggressive and performance aggressive
  ITAP+PATS

## Slide 26: Static Energy Savings
ITAP reduces the static energy by 36.3% compared to CPG and by 27.6% compared to PATS
Peek-ahead improves the ITAP energy savings
by 24.3%
PATS defragments the idle periods and improves the opportunity of applying more powerful power reduction modes in ITAP
ITAP+PATS: additional 9.1% compared to ITAP
2.4%
14.2%
19.4%
37.9%
42.9%
43.6%

## Slide 27: Performance Overhead
ITAP has low performance overhead compared to CPG and PATS
ITAP has up to 2% performance overhead compared to no static power reduction
CPG has up to 41% performance overhead
PATS has up to 12% performance overhead
74.4%
97.4%
83.1%
98.8%
99.6%
99.1%

## Slide 28: Also in the paper…
Different optimization goals of ITAP
  Power-aggressive
  Performance-aggressive
Detailed analysis of hardware overheads
Sensitivity analysis on
  ITAP’s prediction parameters
  SIMD lane size
  ITAP granularity
  Effect of Twake_up and Tbreak_even

## Slide 29: Outline
ion and Goal
Background
Motivation
Inefficiency of Prior Works
ITAP
Evaluation
Conclusion
Notes: Here is the outline for the talk today [CLICK]

## Slide 30: Executive Summary
Motivation: GPU execution units are frequently idle
  Full-lane and partial-lane idleness
  High static power
Problem: static energy represents a high percentage of the energy consumption on execution units
Key idea: Employ the most efficient power management mode for each idle period
Mechanism: Predict the idle period length and apply power-gating and different levels of voltage-scaling
Results:
  27.6% more static energy savings than the state-of-the-art mechanisms
  Less than 2.1% performance overhead

## Slide 31: ITAP: Idle-Time-Aware Power Management for GPU Execution Units
Mohammad Sadrosadati | Seyed Borna Ehsani
Hajar Falahati | Rachata Ausavarungnirun
Arash Tavakkol | Mojtaba Abaee
Lois Orosa Hamid Sarbazi-Azad | Yaohua Wang Onur Mutlu